Laser position in the FTPCs

A.Lebedev,   BNL   04.18.2005

I recovered old data and engineering drawings to establish position of laser beams in the FTPCs. If we are looking on FTPC body from RDO side, we have 3 laser rafts, each of this raft has 5 mirrors. Rafts installed approximately at 4 o’clock, 8 o’clock and 11 o’clock, later I’ll call them   #4, #8, #11.

There is a part of engineering drawing. I put STAR coordinate axis. There is a setup for West FTPC, for East FTPC X-axis will have direction on left, Y axis is always looking upwards.

There is a mirror numbering in the laser raft, which is started from pad plane. Please note that

mirrors 1 and 5 are to create inclined beams. Volker and me did a measurements of laser spots in the gaps of Al pipes, which forms an electrical field in the FTPC volume. We did measurement at RDO side for West FTPC and both RDO and entrance window for East FTPC. I tried to have laser beams in one plane, but its appeared to be difficult task. After this I relied on engineering drawings to calculate radius of laser beams in the middle of last padrow. I estimates that my accuracy is ~ 0.3mm. After this I find a main axises of laser rafts and can calculate X and Y in global STAR coordinate system. These data are not so accurate, because I assume 5 laser beams are in one plane. Later this summer I am planning to open both FTPCs and measure coordinates of laser beams on both sides.

Also I’ll put more data  for padmonitor, when we’ll have 15 beams for each FTPC

West FTPC

There is a table with radius position for lasers

Radius, cm               raft   #4                       #8                   #11               Joern’s data

Mirror   (beam)

1  inclined             27.56                    27.41               27.41

2   straight             28.56                    28.51               28.41              28.59,      28.55

3   straight             19.545                  19.445             19.345            19.55       19.42

4   straight             11.875                  11.675             11.775            11.91       11.48

5   inclined            12.825                  12.675             12.725

Absolute position at last pad row  Z=200cm???

Raft                                            #4                                   #8                          #11

Coordinates, cm                X          Y                        X           Y                     X           Y

Mirror

1                                 26.65         -7.01              -21.73        -16.71            -7.01        26.45

2                                 26.61         -7.27              -22.60        -17.38            -7.27        27.46

3                                 18.90         -4.97              -15.41        -11.86            -4.95        18.70

4                                 11.48         -2.92              -9.25          -7.12              -3.01        11.38

5                                 12.40         -3.16              -10.05        -7.73              -3.26        12.30

Lasers as seen at  padmonitor.  Note a mirror order in table due to inclined beams

Run 4024025                                                   Run6069052      Run   6119019

Raft #4         sector 2,    RDO 2,   RC3

Mirror           pad #                 time bucket #

2                  122                         13                         14                            16

1                  122                          31                        30                            32

3                  121                        111                        110                          112

5                  122                        158                        157                          159

4                  122                        165                        163                          165

Raft #8         sector 4,  RDO7,  RC2

Mirror           pad #                   time bucket #

2                no signal                                                 14                            14

1                   141                               31                   32                            32

3                   141                              111                 109                           111

5                   141                              157                 156                           157

4                   139                              165                 163                           164

Raft #11    sector  6, RDO9,  RC3

Mirror           pad #                   time bucket #

2              no signal                                                no signal                  no signal

1              no signal

3                    120                                113

5                    122                                158

4                     120                               167

East FTPC

There is a table with radius position for lasers

Radius, cm               raft   #4                       #8                   #11               Joern’s data

Mirror   (beam)

1  inclined             27.51                    27.41               27.539

2   straight             28.41                    28.41               28.31

3   straight             19.44                    19.44               19.445            NO DATA

4   straight             11.75                   11.85               11.855

5   inclined            12.65                   12.75               12.75

Absolute position at last pad row  Z=200cm???

Raft                                            #4                                   #8                          #11

Coordinates, cm                X          Y                        X           Y                     X           Y

Mirror

1                                 -27.57         -7.00              21.73        -16.71            7.052        26.64

2                                 -27.47         -7.23              22.52        -17.32            7.244        27.37

3                                 -18.80         -4.95              15.41        -11.85            4.974        18.79

4                                 -11.36         -2.99               9.39          -7.22             3.032        11.46

5                                 -12.23         -3.22              10.11         -7.77             3.262        12.33

Lasers as seen at  padmonitor.  Note a mirror order in table due to inclined beams

Run 4024025                                                             Run 6096052          Run 6119019

Raft #4         sector 2,    RDO 2,   RC3

Mirror           pad #                 time bucket #

2                  no signal

1                  no signal

3                   39                        111

5                   40                        158

4                   40                        166

Raft #8         sector 4,  RDO7,  RC2

Mirror           pad #                   time bucket #

2                no signal

1                no signal

3                no signal

5                no signal

4                no signal

Raft #11    sector  6, RDO9,  RC3

Mirror           pad #                   time bucket #

2                     38                                  15                      16                                  15

1              no signal                                                         29                                  30

3                    120                                113                    109                                112

5                    122                                158                    158                                 no signal

4                     120                               167                    163

# Text boxes

#11

#8

#4

Y

X

5

4

3

2

1