## Slide 1: A possible Design for a forward RICH

## Slide 2: A RICH @ STAR
Main physics interests
  Flavour separation for transverse asymmetries
  Spin transfer measurements
  eRHIC: hadrons at high rapidity for 5 GeV x 100 GeV
Important Considerations
  Momentum resolution  Talk by Anselm
  Space constrains
  Needed momentum coverage
  Impact of fringe magnetic field on photon detector

## Slide 3: Needed Momentum Coverage
100GeV x 100GeV
250GeV x 250GeV
Decadal Plan:
concentrate on 2<rapidiy<4
Momentum Coverage needed:
1-100 GeV
In general needs are very
similar to RICH detectors in
fixed target experiments or
forward spectrometers

## Slide 4: THE FAMILY OF RICH COUNTERS
With focalization
Extended radiator
(gas)
the only approach
at high momenta
(p > 5-6 GeV/c)
EXAMPLES: SELEX,
OMEGA, DELPHI, SLD-CRID, HeraB,
HERMES, COMPASS, LHCb
Proximity focusing
thin radiator
(liquid, solid)
Effective at low
momenta
(p < 5-6 GeV/c)
EXAMPLES: STAR,
ALICE HMPID,
CLEO III
DIRC (Detection of Internally Reflected Cherenkov light)
Quartz as radiator and as light guide
Effective at low momenta
(p < 5-6 GeV/c)
The only existing DIRC was in
operation at BABAR
PANDA is planning two

## Slide 5: RICH Design Equations
Cherenkov threshold equation: cos qc= 1/bn
All light is emitted at a fixed Cherenkov angle to the direction of flight of a particle
qc=√(2d-1/g2) d=n-1 radiator index of refraction
g particle velocity
Npe=N0Lqc2 L radiator length
N0 figure of merit
Transforming that light to the focal plane of a mirror transforms a ring in angle space to a ring in coordinates
R=Fqc F mirror focal length
Single photon counting - statistics really applies (no charge sharing)
s<R>=sR/√(NPE) sR photon pixel resolution
Isochronous - all photons reach the focal plane at the same time

## Slide 6: SINGLE PHOTON DETECTORS
the requests:
QE: high QE (above standard PMT photocathodes having peak-values of 20-25 %)
r: rate capabilities (> 100 kHz/ mm2)
t: time resolution below 100 ps
B: insensitivity to high magnetic fields (B=1T and more)
$: reasonable costs to make large systems affordable
L: Large area and wide angular acceptance of each single sensor
the approaches:
Poly- and nano-crystalline diamond-based photocathodes (QE)
Photocathodes based on C nanotubes (QE)
Hybrid avalanche photodiodes HAPD (B)
Si photomultipliers (QE,r,t,B)
Microchannel plate (MCP) PMTs (B,t)
Micro Pattern Gas Detectors (MPGD) + CsI (r, B, $)
Large, wide aperture (hybride) PMTs (L)
astroparticle experiments
promising
for a far
future

## Slide 7: SINGLE PHOTON DETECTORS
single photon detectors :
the CENTRAL QUESTION since the beginning of the RICH era
3 groups (with examples, not exhaustive lists)
Vacuum based PDs
PMTS (SELEX, Hermes, BaBar DIRC)
MAPMTs (HeraB, COMPASS RICH-1 upgrade)
  Flat pannels (various test beams, proposed for CBM)
Hybride PMTs (LHCb)
MCP-PMT (all the studies for the high time resolution applications)
Gaseous PDs
Organic vapours - in practice only TMAE and TEA (Delphi, OMEGA, SLD CRID, CLEO III)
Solid photocathodes and open geometry (HADES, COMPASS, ALICE, JLAB-HALL A)
Solid photocathodes and closed geometries (PHENIX HBD, even if w/o imaging)
Si PDs
Silicon PMs (only tests till now)

## Slide 8: LARGE SENSITIVE AREAS ↔ GASEOUS PDs
photoconverting vapours are no longer in use, a part CLEO III
(rates ! time resolution !)
the present is represented by MWPC (open geometry!) with CsI
  the first prove (in experiments !) that coupling solid photocathodes and gaseous detectors works
  Severe recovery time (~ 1 d) after detector trips ion feedback 
  Aging CsI ion
  Moderate gain: < 105 (effective gain: <1/2) bombardment
The way to the future: ion blocking geometries
  GEM/THGEM allow for multistage detectors
    With THGEMs: High overall gain ↔ pe det. efficiency!
    Good ion blocking (up to IFB at a few % level)
    MHSP: IFB at 10-4 level
      opening the way to the physicists’ dream (Philosopher’s Stone):
      Gaseous detectors with solid photocathodes for visible light
    (this is for far future)
  PHENIX HBD – first application
  noise performance: pedestal rms 0.15 fC or 0.2 p.e. at a gain of 5000,
  but several pe/channel
  Photon detector – 1 m2

## Slide 9: RADIATOR MATERIALS
the “low momentum” domain <10 GeV/c: Aerogel vs quartz
  Aerogel
    Separation up to higher momenta (but Rayleight, transmission …)
    Lower density  smaller perturbation of particle trajectories, limited number of photons (variable index of refraction to partially overcome)
    Progresses in aerogel production
  Quartz
    q saturation at lower momenta (but removing chromaticity…)
    high density  large number of photons, trajectory perturbation
    excellent transparency, excellent mechanical characteristics 
    detectors of the DIRC family
the “high momentum” domain > 10 GeV/c: gas radiators
    low density gasses for the highest momenta or the best resolutions (NA62)
    Still a major role played by C-F gasses; availability of C4F10 …
    Gas systems for purity (transparency) and pressure control

## Slide 10: AEROGEL NEWS I
News from NOVOSIBIRSK
PRODUCTION STATUS
~2000 liters have been produced for KEDR ASHIPH detector, n=1.05
blocks 20020050 mm have been produced for LHCb RICH, n=1.03
~200 blocks 11511525 mm have been produced for AMS RICH, n=1.05
n=1.13 aerogel for SND ASHIPH detector
n=1.008 aerogel for the DIRAC
3-4 layers focusing aerogel
High optical parameters (Lsc≥43mm at 400 nm)
Precise dimensions (<0.2 mm)

## Slide 11: AEROGEL NEWS II
News from JAPAN
3rd generation:2002- A-RICH for Belle
upgrade (new solvent)
Home made !
largely improved transparency
very good homogeneity both density and chemical comp.
2-layer samples
4th generation:
high density aerogel
prototype result with
3 GeV/c pions
2005 sample
2001 sample
n~1.050
photon yield is not limited by radiator transparency up to ~50mm
n = 1.045
n = 1.050
160mm
transmission length(400nm): 46mm
n = 1.22
60x35x10mm3
transmission length: 18mm at 400nm

## Slide 12: COMPASS RICH-1
p
K
p
in operation
at COMPASS
since 2001
PERFORMANCES:
photons / ring
(b ≈ 1, complete ring in
acceptance) : 14
sq-ph (b ≈ 1) : 1.2 mrad
sring (b ≈ 1) : 0.6 mrad
2s p/K separation @ 43 GeV/c
PID efficiency > 95%
(q particle > 30 mrad)
5 m
6 m
3 m
mirror
wall
vessel
radiator:
C4F10
photon
detectors:
CsI MWPC
Single Radiator: C4F10

## Slide 13: COMPASS RICH-1 – UPGRADE 1/2
Large uncorrelated background
in the forward direction
(m beam halo)
UPGRADE
overlap
of event
images

## Slide 14: COMPASS RICH-1 – UPGRADE 1/2
Technical data
Hamamatsu 16 anode PMTs
(R7600 – UV extended glass)
quartz optics
surface ratio 1:7 ($ !)
wide angular acc. (± 9.5 degrees)
high sensitivity pre-amplifier
fast, high time resolution digital electronics
dead zone: 2% even with 46 mm pitch
About performance
photons / ring (b ≈ 1, complete ring
in acceptance) : 56
time resolution better than 1 ns
sq-ph (b ≈ 1) : 2 mrad
sring (b ≈ 1) : 0.3 mrad
2s p/K separation @ 55 GeV/c
PID efficiency > 95% (also < 30 mrad)
photons
MAPMT
concentrator
field lens
online event
display

## Slide 15: HERA-B Photon Detector
10 m
4 m
Used a lens system to increase active to dead area of photon detector

## Slide 16: Most Relevant RICH Design for STAR
LHC-b: 2 RICHs with 3 radiators

## Slide 17: LHC-b: 2 RICHs with 3 radiators
RICH-1 (modern HERMES RICH) RICH-2
2<p<60 GeV 17<p<100 GeV
25-300 mrad 10-120 mrad
5cm Aerogel (n=1.030) ~200 cm CF4 (n=1.0005)
85 cm C4F10 (n=1.0014)

## Slide 18: LHC-b HPD based Photondetector
3 m2 area have been equipped with photodetectors providing:
Single Photon Sensitivity (200 - 600nm)
2.5 x 2.5 mm2 granularity
Fast readout (40 MHz)
Active-area fraction > 70%
Hybrid Photo Diodes (HPD)
  168 HPDs RICH1
  262 HPDs RICH2
340 k channels

## Slide 19: LHC-b HPD based Photondetector
HPD combines vacuum photo-cathode technology with solid state technology
Photoelectron, released from a photo-cathode, is accelerating by an applied 20kV voltage onto silicon detector. Then it creates ~3000-5000 electron-hole pairs.
The light pattern incident on the photo-cathode is imaged onto silicon matrix.
No dead regions
30% QE at 200 nm
Fast signal (rise-fall times of a few ns) and negligeable jitter
(<1 ns)

## Slide 20: LHC-b RICH performance
Stunning performance  For Details
https://twiki.cern.ch/twiki/bin/view/LHCb/LHCbRICH

## Slide 21: Summary
The RICH-1 concept of LHC-b is ready to go for STAR and eRHIC-detector without enormous R&D
If we drop the Aerogel there could be interesting R&D for the photon detector by making it a GEM
  No sensitivity to magnetic field
  An R&D discussed in the LoI proposal for EIC
  https://wiki.bnl.gov/conferences/index.php/EIC_R%25D
So if we decide a RICH is important for the pp physics program there are good designs available we can rely on
For eRHIC a RICH in forward and backward direction is a must
Most critical momentum resolution qc=√(2d-1/g2)
LHC-b
momentum resolution

## Slide 22
BACKUP

## Slide 23: TECHNOLOGICAL ASPECTS
Radiator materials
  aerogel material (BELLE upgrade, super B factory)
    radiation hardness of fused silica (future DIRCs in PANDA)
    gas systems (C-F gasses: DIRAC, LHCb)
Mirrors & optics
    construction of light mirrors (LHCb)
    Mirror reflectivity (MAGIC)
    Mirror alignment monitoring (COMPASS, LHCb)
    Mirror alignment adjustment (COMPASS)
    (Dichroic) mirrors for focusing DIRC and TOP approaches
Electronics
    Self-triggered read-out electronics (CBM)
    Fast electronics (COMPASS)

## Slide 24: Needed Momentum Coverage

## Slide 25: What is the best Detector concept
Energy loss dE/dx
Cerenkov Radiation
Too small p lever arm
Match radiator and lepton p-range
Transition Radiation:
sensitive to particle g (g>1000)
Aerogel; n=1.03
C4F10; n=1.0014
e
Talk by M. Hartig on the ALICE TRD project

## Slide 26: ALICE Experiment: PID Capabilities
(relativistic rise)
TPC: (dE/dx) = 5.5(pp) – 6.5(Pb-Pb) %
TOF:  < 100 ps
TRD:  suppression  10-2 @ 90% e-efficiency

## Slide 27: Transition Radiation Detector
Radiator:
  irregular structure
  - Polypropylen fibers
  - Rohacel foam (frame)
  4.8 cm thick
  self supporting
Gas:
  Xe/CO2 85/15 %
Drift region:
  3 cm length
  700 V/cm
  75 mm CuBe wires
Amplification region:
  W-Au-plated wires 25 mm
  gain ~ 10000
Readout:
  cathode pads
  8 mm (bending plane)
  70 mm in z/beam-direction
  10 MHz
Schematic View

## Slide 28: Transition Radiation Detector
Large area chambers (1-1,7 m²)
-> need high rigidity
Low rad. length (15%Xo)
-> low Z, low mass material
Design

## Slide 29: Electron Identification Performance
LQ Method:
Likelihood with total charge
LQX Method:
total charge + position of max. cluster
Typical signal of single particle
PID with neural network
e/-discrimination < 10-2
  For 90% e-efficiency
Result of Test Beam Data

## Slide 30: Offline Tracking Performance
dNch/dy = 6000
Efficiency:
high software track-finding
efficiency
lower combined track efficiency
(geometrical acceptance, particle
decay )
Efficiency independent of track
multiplicity
Momentum resolution:
long lever arm ITS + TPC +TRD
(4cm <r<370cm)
resolution better for low
multiplicity (p+p)
pt/pt  5 % at 100 GeV/c and
B = 0.5 T
Efficiency and Resolution for Pb+Pb