## Slide 1: 2013 Spin Patterns, abort Gaps and so on

## Slide 2: Questions TO Answer
Can we change the spin patterns without an impact on our relative luminosity determinations
  WHY: want to fill two RHIC bunches with two AGS bunches at once
    advantage:
    shorter filling time
    2012: 4x109x2=872s
    2013: B1xY1a=436s B1xY1b=488s 2012-patterns:652s
    less bunch growth  impact on ramp eff. and luminosity
Do we want to keep the relation CDEV info corresponds to spin direction at the source untouched
  yes, but we need to make a documentation of
    relation spin direction source to STAR / PHENIX
      document # spin flips source to IP-12 and STAR / PHENIX
    spin rotator settings
    proposal have this page on the polarimeter wiki page  ELKE

## Slide 3: 2012 Situation
4 spin patterns per beam
Blue:
1 +-+--+-++-+- also before 2012
2 -+-++-+--+-+ also before 2012
3 ++--++--++--
4 --++--++--++
Yellow:
1 ++--++--++-- also before 2012
2 --++--++--++ also before 2012
3 +-+--+-++-+-
4 -+-++-+--+-+
we did collide
P1: B1xY1 P5: B3xY3
P2: B2xY1 P6: B3xY4
P3: B1xY2 P7: B4:Y3
P4: B2xY2 P8: B4:Y4
attention: P7: 38/39 missing in yellow, 78/79 in blue
What else:
360 buckets, every 3rd filled
 120 bunches
aboard gaps aligned in PHENIX
anti-aligned in STAR
bunch 38/39 missing in blue
bunch 78/79 missing in yellow
IP12 1-81
IP-6 1-81
IP-10 1-41
IP-2 1-1
IP-8 1-1
IP-4 1-41
blue clockwise
yellow counter clockwise

## Slide 4: 2012 Continued
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|
10
20
30
40
50
60
70
80
90
100
110
120
P1: as example
Blue
Yellow
PHENIX
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
90
100
110
120
10
20
30
40
50
60
70
80
Yellow
STAR
Dropped Bunches Colliding bunches
P1: Y: 5+/6- B: 6+/5- STAR: 102x102 PHENIX: 107x107
P2: Y: 5+/6- B: 5+/6- STAR: 102x102 PHENIX: 107x107
P3: Y: 6+/5- B: 6+/5- STAR: 102x102 PHENIX: 107x107
P4: Y: 6+/5- B: 5+/6- STAR: 102x102 PHENIX: 107x107
P5: Y: 6+/5- B: 5+/6- STAR: 102x102 PHENIX: 107x107
P6: Y: 5+/6- B: 5+/6- STAR: 102x102 PHENIX: 107x107
P7: Y: 7+/4- B: 6+/5- STAR: 100x100 PHENIX: 107x107
P8: Y: 5+/6- B: 6+/5- STAR: 102x102 PHENIX: 107x107
green bunches: empty bunches

## Slide 5: 2012 Spin Pattern
-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|
10
20
30
40
50
60
70
80
90
100
110
120
+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|
10
20
30
40
50
60
70
80
90
100
110
120
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|+-+--+-++-|+--+-++-+-|-+-++-+--+|-++-+--+-+|
10
20
30
40
50
60
70
80
90
100
110
120
1
2
3
4
1
2
3
4
green bunches: empty bunches

## Slide 6: 2013 Proposal
4 spin patterns per beam
Blue:
1 ++--++--++--
2 --++--++--++
3a --++++----++++--
4a ++----++++----++
3b -++--++--++-
4b +--++--++--+
Yellow:
1a --++++----++++--
2a ++----++++----++
1b -++--++--++-
2b +--++--++--+
++--++--++--
--++--++--++
we will collide
P1: B1xY1a/b P5: B3a/bxY3
P2: B2xY1a/b P6: B3a/bxY4
P3: B1xY2a/b P7: B4a/b:Y3
P4: B2xY2a/b P8: B4a/b:Y4
What else:
360 buckets, every 3rd filled
 120 bunches
aboard gaps aligned in PHENIX
anti-aligned in STAR
bunch 70/71 empty in blue
bunch 30/31 empty in yellow
(fixed for e-Lense)
IP12 1-81
IP-6 1-81
IP-10 1-41
IP-2 1-1
IP-8 1-1
IP-4 1-41
blue clockwise
yellow counter clockwise

## Slide 7: 2013 Spin Pattern
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|
10
20
30
40
50
60
70
80
90
100
110
120
++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|
10
20
30
40
50
60
70
80
90
100
110
120
1 5+6-
2 6+5-
3a 5+6-
4a 6+5-
3b 6+5-
4b 5+6-
-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|
+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|
++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|
1a 5+6-
2a 6+5-
1b 6+5-
2b 5+6-
3 5+6-
4 6+5-
-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|
+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|+--++--++-|-++--++--+|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
green bunches: empty bunches

## Slide 8: 2013 Continued
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|
--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|
90
100
110
120
10
20
30
40
50
60
70
80
P1: as example
Blue
Yellow
PHENIX
Yellow
STAR
Dropped Bunches Colliding bunches
P1: Y: 5+/6- 6+/5- B: 5+/6- STAR: 100x100 PHENIX: 107x107
P2: Y: 5+/6- 6+/5- B: 6+/5- STAR: 100x100 PHENIX: 107x107
P3: Y: 6+/5- 5+/6- B: 5+/6- STAR: 100x100 PHENIX: 107x107
P4: Y: 6+/5- 5+/6- B: 6+/5- STAR: 100x100 PHENIX: 107x107
P5: Y: 5+/6- B: 5+/6- 6+/5- STAR: 100x100 PHENIX: 107x107
P6: Y: 6+/5- B: 5+/6- 6+/5- STAR: 100x100 PHENIX: 107x107
P7: Y: 5+/6- B: 6+/5- 5+/6- STAR: 100x100 PHENIX: 107x107
P8: Y: 6+/5- B: 6+/5- 5+/6- STAR: 100x100 PHENIX: 107x107
green bunches: empty bunches

## Slide 9: SUMMARY
spin patterns 1 and 2 in combination with patterns 3b and 4b
  would result in always same or always opposite helicity patterns in either even or odd bunch crossings.
    would not be able to calculate asymmetries separately for even and odd crossings on a fill-by-fill basis.
    don’t want patterns 3b and 4b
spin patterns 1 and 2 in combination with patterns alternative 2013 3 and 4 does not work (see backup)
  reason do not drop equal numbers of + and – bunches
    not changeable as e-Lense needs bunch 30/31 in yellow empty
spin patterns 1 and 2 in combination with patterns 3a and 4a works

## Slide 10: 2013 Alternative Proposal
4 spin patterns per beam
Blue:
1 ++--++--++--
2 --++--++--++
3 ++++----++++--
----++++----++
Yellow:
1 ++++----++++--
----++++----++
++--++--++--
--++--++--++
we will collide
P1: B1xY1 P5: B3xY3
P2: B2xY1 P6: B3xY4
P3: B1xY2 P7: B4:Y3
P4: B2xY2 P8: B4:Y4
What else:
360 buckets, every 3rd filled
 120 bunches
aboard gaps aligned in PHENIX
anti-aligned in STAR
bunch 70/71 empty in blue
bunch 30/31 empty in yellow
(fixed for e-Lense)
IP12 1-81
IP-6 1-81
IP-10 1-41
IP-2 1-1
IP-8 1-1
IP-4 1-41
blue clockwise
yellow counter clockwise

## Slide 11: 2013 Alternative Spin Pattern
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|
10
20
30
40
50
60
70
80
90
100
110
120
----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|
10
20
30
40
50
60
70
80
90
100
110
120
1 5+6-
2 6+5-
3 4+7-
4 7+4-
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
1 4+7-
2 7+4-
3 5+6-
4 6+5-
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
green bunches: empty bunches
++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|
----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|

## Slide 12: 2013 Alternative Continued
++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|++--++--++|--++--++--|
10
20
30
40
50
60
70
80
90
100
110
120
10
20
30
40
50
60
70
80
90
100
110
120
90
100
110
120
10
20
30
40
50
60
70
80
P1: as example
Blue
Yellow
PHENIX
Yellow
STAR
Dropped Bunches Colliding bunches
P1: Y: 4+/6- B: 5+/6- STAR: 100x100 PHENIX: 107x107
P2: Y: 4+/6- B: 6+/5- STAR: 100x100 PHENIX: 107x107
P3: Y: 6+/4- B: 5+/6- STAR: 100x100 PHENIX: 107x107
P4: Y: 6+/4- B: 6+/5- STAR: 100x100 PHENIX: 107x107
P5: Y: 5+/6- B: 4+/7- STAR: 100x100 PHENIX: 107x107
P6: Y: 6+/5- B: 4+/7- STAR: 100x100 PHENIX: 107x107
P7: Y: 5+/6- B: 7+/4- STAR: 100x100 PHENIX: 107x107
P8: Y: 6+/5- B: 7+/4- STAR: 100x100 PHENIX: 107x107
green bunches: empty bunches
++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|
++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|++++----++|++----++++|----++++--|--++++----|